## Slide 1: ECE 571 Final Project
Design Verification of DDR3 Memory Controller
Ajna Bindu R
Jyothsna K
Rithvik M B
Vadiraja M N

## Slide 2: INTRODUCTION
Verification of a Memory Controller interfaced with a DDR3 Memory Model
Object Oriented approach
Verification Environment
SystemVerilog Assertions
Emulation of DDR3 Memory Controller

## Slide 3: PROJECT GOALS
Protocol verification
Timing parameters
Emulation in TBX Mode

## Slide 4: VERIFICATION ENVIRONMENT

## Slide 5: VERIFICATION STRATEGY
Directed Testcases
      Reset – Garbage Data
      Verify single write and read
      Overwrite data on the same address and read
      Write to same row, different column and read
      Write to different row, same bank
      Write to consecutive rows
      Single write to every bank
Generated random testcases

## Slide 6: VERIFICATION STRATEGY
Assertions
Concurrent Assertions
  Write Assertions: Verified the timing parameters T_RCD,T_WL, T_RC
  Read Assertions: Verified the timing parameters T_CL,T_RP
Immediate assertions

## Slide 7: VERIFICATION STRATEGY
INPUT COVERAGE
  To check the tested and untested portion of the design
  Coverage model is defined using covergroup construct
  Implemented for signals at interface and top level
FUNCTIONAL COVERAGE
  Implemented to verify the state transitions of FSM (DUT)

## Slide 8: EMULATION
Implemented Emulation on Veloce using TBX Mode

## Slide 9: STATISTICS

## Slide 10: CONCLUSION
Results: Effective testcases- improved functional coverage
Efficient usage of System Verilog constructs
Bottlenecks:
  Implementation of interfaces between DUT & Testbench
  Emulating the DUT

## Slide 11: REFERENCES
1GB Automotive DDR3L SDRAM Micron datasheet
http://www.verificationguide.com/p/systemverilog-tutorial.html
http://www.testbench.in/
Emulation: PSU Veloce Examples